## Slide 1: How to Succeed @ Lab 5
CSE140L

## Slide 2: Summary
1) Data_memory[64:70] contains ASCII underscore characters (0x5F) encrypted with a "rolling" LFSR code.
  dat_mem[64] = 0x5F ^ {2'b0,LFSR0}, where LFSR0 = initial state of LFSR
  dat_mem[65] = 0x5F ^ {2'b0,LFSR1}, where LFSR1 = next LFSR state
  ...
  dat_mem[70] = 0x5F ^ {2'b0,LFSR6}
2) Your circuit needs to figure out LFSR0, then which LFSR feedback taps were used, then decode the message itself, which starts in encrypted form at dat_mem[71]

## Slide 3: Suggested program phases
1) Determine encoder's LFSR starting value, LFSR[0]
  raddr=64 (read address pointer for data_memory)
  LFSR[0] = 6'h1F ^ dat_out[5:0];
    because LFSR_start ^ 6'h1F ^ 6'h1F = LFSR_start (we love XOR!)
2) Determine next 6 LFSR values, one per clock cycle
  raddr=65, 66, ... , 70
  LFSR[1, 2, ..., 6] = 6'h1F ^ dat_out[5:0];
3) figure out which of 6 LFSR tap patterns the encoder used
  suggest: build 6 parallel LFSRs, one per tap pattern, all advance once/clk cycle
  exactly one of these will match LFSR[6] at 7 clock cycles

## Slide 4: Program phases, continued
4) decode the message, one character / clock cycle
  raddr = 71, 72, ..., 125
  waddr = 0, 1, ..., 60
  dat_in = {2'b0,LFSR[8, 9, ..., 68]} ^ dat_out;

## Slide 5: Final step (Part 2)...
5) remove up to 12 leading _ from message, on character / clock cycle
  raddr = 0, 1, ... , 60
  for(i=0; i<12; i++)
    if(dat_out == 0x5F) raddr++;
    else break; // keep terminal value of i
  if(i==0) $stop; // done
  else for waddr=0, 1, ..., 60 raddr=waddr+i
// this is one/clock cycle read then copy to a lower address